## Slide 1: CSE 431 Computer Architecture Fall 2005 Lecture 05: Basic MIPS Architecture Review
Mary Jane Irwin ( www.cse.psu.edu/~mji )
www.cse.psu.edu/~cg431
[Adapted from Computer Organization and Design,
Patterson & Hennessy, © 2005, UCB]
Notes: Other handouts
To handout next time

## Slide 2: Review: THE Performance Equation
Our basic performance equation is then
CPU time = Instruction_count x CPI x clock_cycle
Instruction_count x CPI
clock_rate
CPU time = -----------------------------------------------
or
These equations separate the three key factors that affect performance
  Can measure the CPU execution time by running the program
  The clock rate is usually given in the documentation
  Can measure instruction count by using profilers/simulators without knowing all of the implementation details
  CPI varies by instruction type and ISA implementation for which we must know the implementation details
Notes: Note that instruction count is dynamic – i.e., its not the number of lines in the code, but THE NUMBER OF INSTRUCTIONS EXECUTED

## Slide 3
So the first area of craftsmanship is in trading function for size. … The second area of craftsmanship is space-time trade-offs. For a given function, the more space, the faster.
The Mythical Man-Month, Brooks, pg. 101

## Slide 4: The Processor: Datapath & Control
Our implementation of the MIPS is simplified
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
Generic implementation
  use the program counter (PC) to supply the instruction address and fetch the instruction from memory (and update the PC)‏
  decode the instruction (and read registers)‏
  execute the instruction
All instructions (except j) use the ALU after reading the registers
How? memory-reference? arithmetic? control flow?
Fetch
PC = PC+4
Decode
Exec
Notes: memory reference use ALU to compute addresses
arithmetic use the ALU to do the require arithmetic
control use the ALU to compute branch conditions.

## Slide 5: MIPS - Registri
32 Registri
Utilizzi preassegnati
Le istruzioni possono utilizzare solo i registri non la memoria (semplificazione sugli indirizzamenti)‏
Istruzioni specifiche di load/store
return
31
$ra
Frame
30
$fp
Stack
29
$sp
Global
28
$gp
temp.
24-25
$t8-$t9
Saved
16-23
$s0-$s7
Temp.
8-15
$t0-$t7
Arguments
4-7
$a0-$a3
Results
2-3
$v0-$v1
Constant 0
0
$zero
Usage
Reg. n.
Name
Pointers
Registro 1?

## Slide 6: MIPS - Istruzioni
Op: Operation code
Rs: First operand register
Rt: Second Operand Register
Rd: Result register
Shamt: Shift amount
Funct: Function, i.e. the variant of the opcode field
Memory reference:
  Load Word (LW)‏
  Store Word (SW)‏
Arithmetic: ù
  Add, Sub
  And,Or
  Slt
Branch:
  Brnch equal (Beq)‏
  Jump (J)‏
op
rs
rt
rd
shamt
funct
Formato delle istruzioni
Esempi di istruzioni
6 bit
5 bit
5 bit
5 bit
5 bit
6 bit
32 bit

## Slide 7: MIPS - Procedure
jal: Jump-and-link
  jal <address>
  Save PC+4 in $ra (address register)‏
jr: Jump Return
  jr $ra
  Ritorna dalla procedura
Stack:
  Registro $sp
$t0-$t9
  Temporary register
  La procedura può cambiarne il contenuto senza bisogno di salvare i dati
$s0-$s7
  Saved register
  La procedura deve salvare i dati prima di utilizzare il contenuto
op
rs
rt
rd
shamt
funct
Istruzioni
Passaggio di parametri
6 bit
5 bit
5 bit
5 bit
5 bit
6 bit
32 bit

## Slide 8: MIPS Esempi di Altri indirizzamenti
op
rs
rd
immediato
6 bit
5 bit
5 bit
16 bit
32 bit
Immediato:
Addi $sp, $sp, 4
$sp=$sp+4
op
address
6 bit
26 bit
32 bit
Salto immediato:
J 10000
Salta all’inidirizzo PC+40000

## Slide 9: MIPS Classificazione dei formati delle istruzioni
Jump
J-format
Tranbsfer/branch/ immediati
I-format
istruzioni Aritmetiche
R-format
Commenti
Campi
Nome
op
address
op
rs
rd
Immediato 16 bit
op
rs
rt
rd
shamt
funct
Immediato 16 bit

## Slide 10: Clocking Methodologies
The clocking methodology defines when signals can be read and when they are written
  An edge-triggered methodology
Typical execution
  read contents of state elements
  send values through combinational logic
  write results to one or more state elements
State
element
1
State
element
2
Combinational
logic
clock
one clock cycle
Assumes state elements are written on every clock cycle; if not, need explicit write control signal
  write occurs only when both the write control is asserted and the clock edge occurs

## Slide 11: Progetto
Assunzioni
Individuazione dei componenti
Datapath
  Soluzioni parziali
  Soluzioni complete
    Single Datapath
    Multicycle Datapath
Microprogramming

## Slide 12: Assunzioni
Limitiamo ad un subset delle operazioni del MIPS (quelle già illustrate)‏
Tempificazione (Clocking Methodology) Edge-triggered

## Slide 13: Componenti (I)‏
Instruction / Data memory
Unità di memoria
Register File
Gestisce la scrittura sull’intero set di registri
In uscita sempre presenti i registri indicati da RR1 e RR”
Per scrivere abilitazione su regWrite e mandare i dati su WD

## Slide 14: Componenti (II)‏
Program Counter
Registro PC
ALU
Unità di Logico Aritmetica
Sign Extend
Estende un valore da 16 a 32 bit
Shift Left/right
Restituiscono lo shift L/R dellingresso

## Slide 15: Costruzione del Datapath
Costruire i datapath parziali per ciascun sottoproblema
Aggregare i datapath per ottenere una soluzione completa
Definire il meccanismo di controllo
Miglioramenti

## Slide 16: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory
  updating the PC to hold the address of the next instruction
Read
Address
Instruction
Instruction
Memory
Add
PC
4
  PC is updated every cycle, so it does not need an explicit write control signal
  Instruction Memory is read every cycle, so it doesn’t need an explicit read control signal

## Slide 17: Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  reading two values from the Register File
    Register File addresses are contained in the instruction

## Slide 18: Executing R Format Operations
R format operations (add, sub, slt, and, or)‏
  perform the (op and funct) operation on values in rs and rt
  store the result back into the Register File (into location rd)‏
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
  The Register File is not written every cycle (e.g. sw), so we need an explicit write control signal for the Register File

## Slide 19: Executing Load and Store Operations
Load and store operations involves
  compute memory address by adding the base register (read from the Register File during decode) to the 16-bit signed-extended offset field in the instruction
  store value (read from the Register File during decode) written to the Data Memory
  load value, read from the Data Memory, written to the Register File
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
16
32

## Slide 20: Executing Branch Operations
Branch operations involves
  compare the operands read from the Register File during decode for equality (zero ALU output)‏
  compute the branch target address by adding the updated PC to the 16-bit signed-extended offset field in the instr
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)‏

## Slide 21: Executing Jump Operations
Jump operation involves
  replace the lower 28 bits of the PC with the lower 26 bits of the fetched instruction shifted left by 2 bits
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
address
26
4
28

## Slide 22: Creating a Single Datapath from the Parts
Assemble the datapath segments and add control lines and multiplexors as needed
Single cycle design – fetch, decode and execute each instructions in one clock cycle
  no datapath resource can be used more than once per instruction, so some must be duplicated (e.g., separate Instruction Memory and Data Memory, several adders)‏
  multiplexors needed at the input of shared elements with control lines to do the selection
  write signals to control writing to the Register File and Data Memory
Cycle time is determined by length of the longest path

## Slide 23: Single datapath
Fondiamo i componenti così ottenuti e cerchiamo di costruire un sistema che isa in grado di eseguire tutte le operazioni indicate.
Procederemo sempre per passi, aggregando le parti un po’ per volta, e poi individuando i segnali di controllo per gestire il flusso dell’esecuzione
Si cercherà di far sì che tutte le istruzioni possano essere eseguite in un solo colpo di clock

## Slide 24: Fusione R-format/i-format(L/S)‏
R-format
I-format

## Slide 25: Fusione R-format/i-format(L/S)‏
R-format
I-format

## Slide 26: Fusione R-format/i-format(L/S)‏
R-format
I-format

## Slide 27: Fusione R-format/i-format(L/S)‏
R-format
I-format

## Slide 28: Fusione R-format/i-format(L/S)‏

## Slide 29: Aggiunta dell’operazione di fetch

## Slide 30: Aggiunta dell’operazione di fetch

## Slide 31: Aggiunta dell’operazione di fetch

## Slide 32: L’istruzione BEQ…

## Slide 33: L’istruzione BEQ…

## Slide 34: DataPath Completo..

## Slide 35: DataPath Completo.. Attenzione!

## Slide 36: MIPS Ricordiamo i formati
Jump
J-format
Tranbsfer/branch/ immediati
I-format
istruzioni Aritmetiche
R-format
Commenti
Campi
Nome
op
address
op
rs
rt
immediato
op
rs
rt
rd
shamt
funct

## Slide 37: DataPath Completo

## Slide 38: Fetch, R, and Memory Access Portions
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 39: Single Cycle Disadvantages & Advantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
  especially problematic for more complex instructions like floating point multiply
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
but
Is simple and easy to understand
Clk
lw
sw
Waste
Cycle 1
Cycle 2
Notes: In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.

## Slide 40: Multicycle Datapath Approach
Let an instruction take more than 1 clock cycle to complete
  Break up instructions into steps where each step takes a cycle while trying to
    balance the amount of work to be done in each step
    restrict each cycle to use only one major functional unit
  Not every instruction takes the same number of clock cycles
In addition to faster clock rates, multicycle allows functional units that can be used more than once per instruction as long as they are used on different clock cycles, as a result
  only need one memory – but only one memory access per cycle
  need only one ALU/adder – but only one ALU operation per cycle

## Slide 41: Multicycle Datapath Approach, con’t
At the end of a cycle
  Store values needed in a later cycle by the current instruction in an internal register (not visible to the programmer). All (except IR) hold data only between a pair of adjacent clock cycles (no write control signal needed)‏
  IR – Instruction Register MDR – Memory Data Register
  A, B – regfile read data registers ALUout – ALU output register
Address
Read Data
(Instr. or Data)‏
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
  Data used by subsequent instructions are stored in programmer visible registers (i.e., register file, PC, or memory)‏
Notes: Have to add multiplexors in front of several of the functional unit inputs because the functional units are shared by different instruction cycles.
Reading/writing to
  any of the internal registers or the PC occurs (quickly) at the end of a clock cycle
  reading/writing to the register file takes ~50% of a clock cycle since it has additional control and access overhead (reading can be done in parallel with decode)‏

## Slide 42: The Five Steps of the Load Instruction
IFetch: Instruction Fetch and Update PC
Dec: Instruction Decode, Register Read, Sign Extend Offset
Exec: Execute R-type; Calculate Memory Address; Branch Comparison; Branch and Jump Completion
Mem: Memory Read; Memory Write Completion; R-type Completion (RegFile write)‏
WB: Memory Read Completion (RegFile write)‏
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
INSTRUCTIONS TAKE FROM 3 - 5 CYCLES!
Notes: As shown here, each of these five steps will take one clock cycle to complete.

## Slide 43: Multicycle Advantages & Disadvantages
Uses the clock cycle efficiently – the clock cycle is timed to accommodate the slowest instruction step
Multicycle implementations allow functional units to be used more than once per instruction as long as they are used on different clock cycles
but
Requires additional internal state registers, more muxes, and more complicated (FSM) control
Clk
Cycle 1
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type

## Slide 44: Single Cycle vs. Multiple Cycle Timing
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type
Clk
Single Cycle Implementation:
lw
sw
Waste
Cycle 1
Cycle 2
multicycle clock slower than 1/5th of single cycle clock due to state register overhead
Notes: Here are the timing diagrams showing the differences between the single cycle and multiple cycle.
In the multiple clock cycle implementation, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.

## Slide 45: Cosa manca??

## Slide 46: Cosa manca??
L’unità di controllo…
Quando e come dare tutti i segnali?

## Slide 47: Datapath - segnali di Controllo MIPS Singolo Ciclo

## Slide 48: I Segnali di Controllo
Write data from memory
Write data from ALU
MemTOReg
Ha come ingresso l’opcode dell’istruzione, effettua la transcodifica nel code accettato dalla CPU
ALUop
Data on the input is written in memory
None
memWrite
Data memory content put on the read output
None
MemRead
The PC given by branch
The PC is (PC+4)‏
PCsrc
The second ALU operand
from instruction
The second ALU operand
from register
ALUsrc
Write Register Enabled
None
RegWrite
The register destination is rd [15-11]
The register destination is rt [20-16]
RegDst
Alto
Basso
Segnale

## Slide 49: Compito dell’unità di controllo
Riceve in ingresso l’opcode ([31-26] della word dell’istruzione) ed emette i segnali per abilitare le varie parti della macchina:
  memRead/memWrite per la memoria dati
  Addr per i vari mux
  ALUop per l’ALU (quale operazione fare)‏
  RegWrite
  …

## Slide 50: Adding the Control
Selecting the operations to perform (ALU, Register File and Memory read/write)‏
Controlling the flow of data (multiplexor inputs)‏
I-Type:
op
rs
rt
address offset
31
25
20
15
0
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
Observations
  op field always in bits 31-26
  addr of registers to be read are always specified by the rs field (bits 25-21) and rt field (bits 20-16); for lw and sw rs is the base register
  addr. of register to be written is in one of two places – in rt (bits 20-16) for lw; in rd (bits 15-11) for R-type instructions
  offset for beq, lw, and sw always in bits 15-0
J-type:
31
25
0
op
target address

## Slide 51: Single Cycle Datapath with Control Unit
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: Note mux control inputs have been swapped (for three of the muxes) from the last picture to be consistent with the book.

## Slide 52: R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 53: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 54: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 55: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 56: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 57: Adding the Jump Operation
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Shift
left 2
0
1
Jump
32
Instr[25-0]
26
PC+4[31-28]
28
Notes: For lecture
Good exam questions
Add jalr rs,rd 0 rs 0 rd 0 9
jump to instr whose addr is in rs and save addr of next inst (PC+4) in rd
Add the PowerPC addressing modes of update addressing and indexed addressing (will have to expand the RegFile to be three read port and two write port)‏
Add andi, ori, addi - have to have both a signextend and a zeroextend and choose between the two, will have to augment the ALUop encoding (since can’t get the op information out of the funct bits as with R-type)‏
Add mult rs, rt with the result being left in hi|lo - so also include the mfhi and mflo instructions (will have to add a multiplier, the hi and lo registers and then a couple of muxes and their control).
Add barrel shifter

## Slide 58: The Multicycle Datapath with Control Signals
Address
Read Data
(Instr. or Data)‏
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
Sign
Extend
Shift
left 2
ALU
control
Shift
left 2
ALUOp
Control
IRWrite
MemtoReg
MemWrite
MemRead
IorD
PCWrite
PCWriteCond
RegDst
RegWrite
ALUSrcA
ALUSrcB
zero
PCSource
1
1
1
1
1
1
0
0
0
0
0
0
2
2
3
4
Instr[5-0]
Instr[25-0]
PC[31-28]
Instr[15-0]
Instr[31-26]
32
28

## Slide 59: Progetto Unità di Controllo del MIPS

## Slide 60: Multicycle Control Unit
Multicycle datapath control signals are not determined solely by the bits in the instruction
  e.g., op code bits tell what operation the ALU should be doing, but not what instruction cycle is to be done next
Must use a finite state machine (FSM) for control
  a set of states (current state stored in State Register)‏
  next state function (determined by current state and the input)‏
  output function (determined by current state and the input)‏
Combinational
control logic
State Reg
Inst
Opcode
Datapath
control
points
Next State
. . .
. . .
. . .

## Slide 61: La Macchina di Controllo
Le “fasi” del processore sono associabili agli ‘stati’ della macchina.
Per compiti differenti abbiamo differenti percorsi dell’automa
In figura visione d’insieme del controllo
In seguito per ogni pezzo analizziamo i diversi stati componenti

## Slide 62: Fetch & Decode
In ogni stato l’elenco dei segnali di controllo emessi
Sugli archi le condizioni di transizione
In figura vediamo le fasi di fetch e decode.
Nota:
  Passaggio obbligato IF-DE
  Dopo DE l’automa si biforca nei vari stati

## Slide 63: Memory Reference
Per le istruzioni di L/S accesso a memoria
Notare evoluzione in più stati …

## Slide 64: Istruzioni R-type
Istruzioni di esecuzione R-type
  Attivazione ALU
  Memorizzazione del risultato

## Slide 65: Branch & Jump
Istruzioni di salto
  Nel primo caso verifica del risultato di confronto
  Nel secondo caso semplice cambiamento del valore del PC
Branch
Jump

## Slide 66: Automa Completo
Schema Completo dell’automa a stati finiti
L’automa ritorna all’origine (operatività infinita
Opera per ‘Fasi’

## Slide 67: Le eccezioni
Cosa accade se il processore supporta le interruzioni?
  La fase di ‘check for interrupt’ …
E’ necessario individuarne la causa (overflow, segnale esterno), verificare le priorità, …

## Slide 68: Datapath con Interruzioni

## Slide 69: Modifica dell’Automa
Aggiunta di stati per:
  la generazione delleccezione (esempio overflow)‏
  Il controllo dei segnali esterni